# Text boxes

Installation:

- Verify that roof surface is smooth and clean to extent needed to receive materials.

- Review approved final drawings to determine the locations of Cable Trays.

- Clean surfaces to receive Cable Tray Supports removing any loose gravel and any foreign matter before setting Cable Tray Supports.

- Accurately locate Cable Tray supports in locations specified as per approved shop drawings or as required by site conditions.

- Attach Cable Trays to Cable Tray Supports and connect to other Cable Trays with splice clamps to form continuous system.

- Adjust height of each Cable Tray Support and correct height if necessary.

- Repeat until all support Cable Trays supplied are installed in accordance with approved shop drawings.

- Remove any unused materials and packaging from job site.

Materials

Cable Trays:  All ASP Cable Trays and components are engineered to work together as a continuous system as well as stand-alone elements.  ASP Cable Trays are available in standard length of 12” with run spacing every 12”.  Easily connects to any ASP cable tray with splice clamps provided.  Standard depth is 4” with optional depth of 6”.

Materials:  Aluminum or hot dip galvanized steel

Options:  Widths of 12”, 18” or 24”; Depths of 4” or 6”; Lengths of 10’ or 12’; Custom sizes available

Accessories:  Cable Tray Supports; Covers in various finishes

This print/image and design and detail shown hereon is the property of Advanced Support Products, Inc. This print is furnished with the understanding that it is not to be reproduced without permission, and must be returned upon demand.  All rights of design and invention are reserved by Advanced Support Products.      Patents #5816554 ;  #6229497;  #6427965;  #6448497;  #6578827  © 2010

Specification Sheet

ASP Cable Trays

Standard Cable Trays