| Model | Dimensions | Weight |
| --- | --- | --- |
|  | A | B |  |
| RCB2409 RCB3609 RCB4809 RCB3613 RCB4813 RCB6013 | 9”/22.86cm 9”/22.86cm 9”/22.86cm 13”/33.02cm 13”/33.02cm 13”/33.02cm | 24”/60.96cm 36”/91.44cm 48”/121.92cm 36”/91.44cm 48”/121.92cm 60”/152.40cm | 18 lb/8.16kg 20 lb/9.07kg 22 lb/9.98kg 27lb/12.25kg 29lb/13.15kg 31lb/14.06kg |

Installation:

- Verify that roof surface is smooth and clean to extent needed to receive materials.

- Review approved final drawings to determine the locations of EcoCurb Supports.

- Clean surfaces to receive EcoCurb Supports removing any loose gravel and any foreign matter before setting EcoCurb Supports.

- Accurately locate and align pre-fabricated EcoCurb supports in locations specified as per approved shop drawings or as required herein and by site conditions to limit pipe and/or conduit deflection to L/240, not to exceed 10' (3m) on center. If Isolation pads are required, place under each EcoCurb Support.

- Should the roofing manufacturer require a separation sheet between the roof and the EcoCurb Support, place a separation sheet or protective pad conforming to the existing roof manufacturer’s system under each EcoCurb Support. Do not adhere to the roof system or to EcoCurb Support.

- Repeat until all supports supplied are installed in accordance with approved shop drawings.

- Remove any unused materials and packaging from job site.

REC-CB – Rubber EcoCurb Cross Brace Bridge – Is designed specifically for use on rooftop without adhesive, roof penetrations, flashings or damage to roofing system.  Designed to support equipment units or a series of pipes.  Strut is bolted directly to EcoCurb support by 1/2” X 3-1/2” Bolts, 1/2” Nuts and Washers.  Strut clamps are suggested to hold piping.

Materials

EcoCurb:  Manufactured from Recycled Rubber, Vulcanized.

LEED:  100% recycled pre-consumer rubber

Frame:  1-5/8” X 1-5/8” 12 ga. channel (ASTM A653) - available in Pre-Galvanized Zinc coated, Hot-Dip Galvanized or Stainless Steel finishes.

Hardware:  1/2” X 3-1/2” Bolts; 1/2” Nuts and Washers available in Pre-Galvanized Zinc coated, Hot-Dip Galvanized or Stainless Steel finishes.

Accessories:  Strut Clamps; Protection Pads

This print/image and design and detail shown hereon is the property of Advanced Support Products, Inc. This print is furnished with the understanding that it is not to be reproduced without permission, and must be returned upon demand.  All rights of design and invention are reserved by Advanced Support Products.      Patents #5816554 ;  #6229497;  #6427965; #6448497; #6578827  © 2010

Specification Sheet

REC-CB

Rubber EcoCurb Cross Brace Bridge