# Text boxes

## VS1610L Ground Site Platform

All ASP platforms are suitable for any undeveloped land

or rooftop site applications unless specified otherwise.

This print/image and design and detail shown hereon is the property of Advanced Support Products, Inc. This print is furnished with the understanding that it is not to be reproduced without permission, and must be returned upon demand.  All rights of design and invention are reserved by Advanced Support Products, Inc.        Patent #5816554 ;  Patent #6229497 ;  Other patents pending.                                                             ©copyright 2001

# Product Name

Advanced Support Products, Inc.

281-357-1277 Phone

800-941-5737 Toll Free

281-357-0577 Fax

www.ASPbase.com

This platform is used to support various type of equipment on ground sites.  The platform is completely grated with the center frame dimensions of 16’0”wX2’8”d.

Material:        Galv. steel; polypropylene bases

Bases:	          20

Weight:	          1870 lbs.

Dimensions:    16' 0" w x 10' 0" d x 12" h (overall)

Options:          Guardrail, ladder, stairs, telco rack, cable hangers,

protection pads

All ASP Inc. products are made to American Society for Testing Materials (ASTM) A 36 steel standards and are galvanized to A 123 or A 153 standards unless otherwise specified.

General Purpose Platform for ground sites only.