# Text boxes

## WF1010L Equipment Platform

All ASP platforms are suitable for any undeveloped land

or rooftop site applications unless specified otherwise.

This print/image and design and detail shown hereon is the property of Advanced Support Products, Inc. This print is furnished with the understanding that it is not to be reproduced without permission, and must be returned upon demand.  All rights of design and invention are reserved by Advanced Support Products, Inc.        Patent #5816554 ;  Patent #6229497 ;  Other patents pending.                                                             ©copyright 2001

# Product Name

Advanced Support Products, Inc.

281-357-1277 Phone

800-941-5737 Toll Free

281-357-0577  Fax

www.ASPbase.com

A general purpose equipment support platform that is completely grated and used on ground sites to support various types of equipment.  Center frame is 10’0”wX3’0”d.  Standard height is 12”, with adjustable legs.

Material:        Galv. steel; polypropylene bases

Bases:	          20

Weight:	          1260 lbs.

Dimensions:    10' 0" w x 10' 0" d x 12" h (overall)

Options:          Guardrail, ladder, stairs, telco rack, cable hangers,

protection pads

All ASP Inc. products are made to American Society for Testing Materials (ASTM) A 36 steel standards and are galvanized to A 123 or A 153 standards unless otherwise specified.

General Purpose Platform for ground sites only.