| Model | Dimensions | Weight |
| --- | --- | --- |
|  | A | B | C |  |
| RSB1818 RSB2418 RSB3618 RSB4818 RSB1824 RSB2424 RSB3624 RSB4824 | 9”/22.86cm 9”/22.86cm 13”/33.02cm 13”/33.02cm 9”/22.86cm 9”/22.86cm 13”/33.02cm 13”/33.02cm | 18”/45.72cm 24”/60.96cm 36”/91.44cm 48”/121.92cm 18”/45.72cm 24”/60.96cm 36”/91.44cm 48”/121.92cm | 18”/45.72cm 18”/45.72cm 18”/45.72cm 18”/45.72cm 24”/60.96cm 24”/60.96cm 24”/60.96cm 24”/60.96cm | 57 lb/25.85kg 59 lb/26.76kg 75 lb/34.02kg 77 lb/34.93kg 58 lb/26.31kg 60 lb/27.33kg 77 lb/34.93kg 79 lb/35.83kg |

Installation:

- Verify that roof surface is smooth and clean to extent needed to receive materials.

- Review approved final drawings to determine the locations of EcoCurb Supports.

- Clean surfaces to receive EcoCurb Supports removing any loose gravel and any foreign matter before setting EcoCurb Supports.

- Accurately locate and align pre-fabricated EcoCurb supports in locations specified as per approved shop drawings or as required herein and by site conditions to limit pipe and/or conduit deflection to L/240, not to exceed 10' (3m) on center. If Isolation pads are required, place under each EcoCurb Support.

- Should the roofing manufacturer require a separation sheet between the roof and the EcoCurb Support, place a separation sheet or protective pad conforming to the existing roof manufacturer’s system under each EcoCurb Support. Do not adhere to the roof system or to EcoCurb Support.

- Repeat until all supports supplied are installed in accordance with approved shop drawings.

- Adjust height of each strut or channel and hanger or roller to its required height and tighten with nut, but do not over-tighten.  Check each support for equal weight disbursement.  Correct if necessary.

- Remove any unused materials and packaging from job site.

This print/image and design and detail shown hereon is the property of Advanced Support Products, Inc. This print is furnished with the understanding that it is not to be reproduced without permission, and must be returned upon demand.  All rights of design and invention are reserved by Advanced Support Products.      Patents #5816554 ;  #6229497;  #6427965; #6448497; #6578827  © 2010

REC-18SB & REC-24SB – Rubber EcoCurb Support Bridge – Is designed specifically for use on rooftop without adhesive, roof penetrations, flashings or damage to roofing system.  Designed to offer stability and adjustability while supporting a series of pipes.  Optional items include suspending hangers from cross bar to support pipe at various heights and using strut clamps or rollers directly on cross bar.

Materials

EcoCurb:  Manufactured from Recycled Rubber, Vulcanized.

LEED:  100% recycled pre-consumer rubber

Frame:  1-5/8” X 1-5/8” 12 ga. channel (ASTM A653) - available in Pre-Galvanized Zinc coated, Hot-Dip Galvanized or Stainless Steel finishes.

Hardware:  Corner Brackets and Leg Brackets bolted with 1/ 2” X

2-1/2” Bolt & 1/2” Nut; Frame bolted to EcoCurb with 1/2” X 3-1/2” Bolts, 1/2” Nuts and Washers. Leg Brackets are available in Hot-Dip Galvanized only, all other hardware available in Pre-Galvanized Zinc coated, Hot-Dip Galvanized or Stainless Steel finishes.

Accessories:  Clevis Hangers, Swivel Hangers; Strut Clamps; Roller Frame with Roller; Protection Pads

Specification Sheet

REC-18SB & REC-24SB

Rubber EcoCurb Support Bridge