# Text boxes

Installation:

- Verify that roof surface is smooth and clean to extent needed to receive materials.

- Review approved final drawings to determine the locations of Antenna Mount.

- Clean surfaces to receive 17” circular bases removing any loose gravel and any foreign matter before setting 17” circular support bases.

- Accurately locate Antenna Mount in location specified as per approved shop drawings or as required herein and by site conditions. No Isolation pads are required under the 17" circular bases.

- Should the roofing manufacturer require a separation sheet between the roof and the support system, place a separation sheet or protective pad conforming to the existing roof manufacturer’s system under 17" circular bases. Do not adhere to the roof system or 17" circular bases.

- Insert steel frame structures into 17" circular bases as indicated in above drawing.

- Adjust height of each support base for equal weight disbursement. Correct if necessary.

- Repeat until all support bases supplied are installed in accordance with approved shop drawings.

- Remove any unused materials and packaging from job site.

ASP301 – Platform Antenna Mount – Is designed specifically for full 360 degree coverage on rooftop without adhesive, roof penetrations, flashings or damage to roofing system.  Combination of cabinet area, grated work area and antenna mast overcome the constraints of small area sites.

Materials

Support Base:  17" circular base, injected molded polypropylene, with 227 sq. in. of surface on bottom, designed for weight displacement.

Base Dimensions: 3"H X 17" in diameter, designed for weight displacement, with molded insert for square tubing and two threaded rod couplings molded in.

LEED: Minimum 40 % post industrial recycled polypropylene with UV inhibitors.

Platform Mount: 4”X4’X1/4” Angle; 4” Ø Schedule 40 Pipe; 1” X 3/16” bar grating, 19-W-4 carbon steel, ends capped with 1” X 1/ 4” steel flat bar; Hot-Dip Galvanized after fabrication.

Hardware:  1/2”X2” Bolts; with 1/2” Nuts and Washers; available in Pre-Galvanized Zinc coated or Hot-Dip Galvanized.

Accessories:  Protection Pads

| Model | Dimensions | Weight |
| --- | --- | --- |
|  | Length | Width | # Mast |  |
| ASP301-360 | 8’7”/2.126m | 8’3”/2.51m | 3 – 8’ H | 590 lb/267.62kg |

Custom sizes and heights are available.

This print/image and design and detail shown hereon is the property of Advanced Support Products, Inc. This print is furnished with the understanding that it is not to be reproduced without permission, and must be returned upon demand.  All rights of design and invention are reserved by Advanced Support Products.      Patents #5816554 ;  #6229497;  #6427965;  #6448497;  #6578827  © 2010

Specification Sheet

ASP301 Antenna Mount

360 Platform Antenna Mount