# Text boxes

## SS1000T Hanging Pipe Support

All ASP pipe supports and components are engineered to work together as a continuous system as well as stand alone elements.

This print/image and design and detail shown hereon is the property of Advanced Support Products, Inc. This print is furnished with the understanding that it is not to be reproduced without permission, and must be returned upon demand.  All rights of design and invention are reserved by Advanced Support Products, Inc.        Patent #5816554 ;  Patent #6229497 ;  Other patents pending.                                                             ©copyright 2001

# Product Name

Advanced Support Products, Inc.

P.O. Box 1287 ● Tomball, Texas ● 77377

Tele. 800.941.5737 ● fax 800.941.5739

www.ASPbase.com

Designed to carry up to (6" pipe.  Hanger mechanism allows for suspending pipe at various heights.  Base is  17" in diameter and is designed to disburse weight over 227 sq. in. per support.  Maximum recommended distance between supports is 10' unless otherwise specified.

Material:  	Polypropylene base, 1-5/8" x 1-5/8" and 1-7/8" x 1-7/8" square strut, 12 ga., ½" allthread, nuts & washer with clevis or swivel hanger for pipe

Dimensions:	18"W x variable height   Weight:  21 lbs.

Accessories:	Protection Pad

All ASP  products are made to American Society for Testing Materials (ASTM) A 36 steel standards and are galvanized to A 123 or A 153 standards unless otherwise specified.